## Slide 1: BITS ZG553: Real Time Systems
K G Krishna
WILP Division, BITS-Pilani, Hyderabad

## Slide 2
Text Book / References
Text Book (T1)
Reference (R1)
Note: As the above two books focus on theoretical treatment of the subject, Students are strongly advised to refer to web sources / MOOCs videos / library within their own organizations for more practical understanding of the topics.

## Slide 3
Excellent MOOCs Videos
(Coursera, edX,…)

## Slide 4
RTS Primer – For Light Reading

## Slide 5
L-5: RTS Scheduling -
Functional/Temporal Parameters, Feasibility & Optimality
Ref: T1/ [C3, Lecture PPT/Notes]
Note: Students are requested to NOT to rely on PPTs/Recorded sessions as their only source of knowledge, explore sources within your own organization or web for any specific topic; attend classes regularly and involve in discussions;
PLEASE DO NOT PRINT PPTs, Save the Environment!
Source PPT Courtesy: Some of the contents of this PPT is sourced from Presentatoons of Prof K R Anupa, BITS-Pilani WILP Faculty

## Slide 6: Ji - Parameters
Temporal
Functional
Resources
Interconnection

## Slide 7
Timing Specifications – Periodic Task
release time (ri)
deadline (Di)
period (p)
Ti
Ti+1
release time(ri+1)
execution time (ei)
execution time (ei+1)
time
deadline (Di+1)
response time
response time

## Slide 8
Timing Specifications – Aperiodic & Sporadic Task
release time (ri)
deadline (Di)
Ti
execution time (ei)
time
response time

## Slide 9: Ji - Parameters
Temporal
Functional
Resources
Interconnection
  Control
  Data
Ji < Jk
Interconnection - Precedence Constraints
Notes: Probability that the task can be released on or before x – for varying values of x
E changes due to cache/pipelines – mpeg no. of bits used to encode a bit.

## Slide 10
Jobs are said to have precedence constraints if they are constrained to execute in some order.
If jobs can execute in any order, they are called independent.
A job Ji is a predecessor of another job Jk if Jk can’t begin execution until the execution of Ji completes. It is denoted by
Ji < Jk
Here Jk is a successor of Ji .
Let us consider the relation Ji < Jj < Jk .
Ji is a immediate predecessor of Jj and predecessors of Jj and Jk
Jk is a immediate successor of Jj and successor of Ji and Jj
A job with predecessors is ready for execution when the time is at or after its release time and all of its predecessors are completed.
Precedence Constraints, Predecessors and Successors

## Slide 11
Precedence Constraints are represented through a graph called ‘Precedence Graph’.
How to draw a precedence graph :
Each vertex in the graph represents a job.
Above each vertex, the feasible interval for the job is mentioned in brackets.
Draw a directed edge (arrowhead) from vertex Ji to Jk if Ji is a immediate predecessor of Jk .
Precedence Graph

## Slide 12
(0,7]
(2,9]
(4,11]
(6,13]
(8,15]
(2,5]
(5,8]
(8,11]
(11,14]
(14,17]
Precedence Graph

## Slide 13
Precedence Graph - Example
J1, J2, J3 and J4 have feasible intervals (0, 6], (5, 8], (2, 8] and (3, 5] respectively
J1 and J4 are predecessors of J2
J3 is neither a predecessor, not a successor of any other jobs
J1 (0, 6]
J2 (5, 8]
J3 (2, 8]
J4 (3, 5]

## Slide 14
T1
T2
T3
T4
T5
T6
T7
T8

## Slide 15
Task Graph is like a Precedence Graph.
Each vertex represents a job, which is indicated by circles and squares.
Above each vertex, the feasible interval for the job is mentioned in brackets.
A sub-graph becomes a chain, when the jobs in the sub-graph need to be serially executed i.e. either Ji < Jk or Ji > Jk .
Unlike precedence graph, the edges are of different types representing different types of dependencies.
The types of an edge connecting two vertices and other parameters of the edge are interconnection parameters of the jobs represented by the vertices.
Task Graph

## Slide 16
In a producer-consumer environment, producer puts the data in a shared memory and the consumer consumes the data from the shared memory.
The precedence graph will show that the producer and consumer are independent, since they are not explicitly constrained for execution.
In task graphs, these two jobs will be connected via data-dependency edges.
Data Dependency

## Slide 17
Difference in completion time of two jobs is called temporal distance.
Example: To have lip synchronization, the time between the display of each frame and the generation of corresponding audio must be now more than 160 ms.
In task graph, temporal distance is represented by temporal dependency edges.
There is a temporal dependency edge from vertex Ji to vertex Jk, if Jk has to be completed after a certain time after Ji completes. The value of this parameter is infinite if there is no temporal dependency between these jobs.
Temporal Dependency

## Slide 18
An AND job is the one which can begin execution at or after its release time provided all of its predecessors has been completed.
AND jobs are represented by unfilled circles in the task graph.
An OR job is the one which can begin execution at or after its release time provided one or some of its immediate predecessors has been completed.
OR jobs are represented by unfilled squares in the task graph. The fraction of the number of predecessor to be completed is indicated below the vertex e.g. if 2 out of 3 jobs are to be completed, then put 2/3 there.
AND / OR Precedence Constraints

## Slide 19
Task Graph - Example
(2, 5]
(5, 8]
(8, 11]
(11, 14]
(0, 5]
(4, 8]
(5, 20]
(11, 14]
(0, 6]
(5, 10]
(6, 15]
(11, 14]
branch
join
(4, 8]
1/2

## Slide 20
The job from which the conditional branch arises is called a branch job.
The job at which the conditional branches join is called a join job.
Both these jobs are represented as filled circles in the task graph.
The sub-graph that begins from the branch job and ends at the join job is called conditional block.
Conditional Branches

## Slide 21
Pipelined relationship is used when between a pair of producer-consumer jobs, data can be piped.
In the task graph, the vertices are the granules of the producer and the consumer.
Each granule of the consumer can begin execution when the previous granule of the job and the corresponding granule of the consumer job is completed.
This relationship is represented by a dotted arrow in the task graph.
Pipeline Relationship

## Slide 22
Task Graph - Example
(2, 5]
(5, 8]
(8, 11]
(11, 14]
(0, 5]
(4, 8]
(5, 20]
(11, 14]
(0, 6]
(5, 10]
(6, 15]
(11, 14]
branch
join
(4, 8]
1/2

## Slide 23
Preemptivity
Criticality
Optional Interval
Laxity type
Functional Parameters

## Slide 24
A job is preemptable if its execution can be suspended at any point of time to allow execution of other jobs and later its execution can be resumed from the point of suspension.
A job is nonpreemptable if it must be executed from start to end without any interruption.
Example: Interrupt Handling is non-preemptable.
Context Switching
During preemption, the system must first save the state of the preempted job, so that it can resume the execution of it later. The state of a job typically includes
  Program Counter Register
  Stack Pointer Register
  Other General Purpose Registers
  …
After doing this, the system must load new processor status register, initialize the program counter, clear the processor pipeline etc.
These actions are called context switching.
Time taken for context switching is called context switch time.
Preemptivity of Jobs

## Slide 25
The criticality or importance of a job, is a positive number, which indicates how critical the execution of the job is, for the system.
Priority and Weights are often used to refer to the criticality.
During overload, when it is not possible to schedule all the jobs to meet their deadline, less critical jobs are sacrificed.
Criticality of Jobs

## Slide 26
A job or a portion of a job can be called optional, if it completes late or not executed at all, the system performance may degrade but nevertheless the function is satisfactory.
During overload, when it is not possible to complete all the jobs on time, we may chose to discard the optional jobs (i.e. leave them unexecuted or partially executed).
The jobs and portion of the jobs which are not optional, are mandatory.
Optional Execution

## Slide 27
Laxity type of a job indicates whether the time constraints are hard or soft.
It is represented by a ‘usefulness function’, which gives the usefulness of the result produced by the job as the function of its tardiness.
If the usefulness of a job becomes zero or negative as soon as the job becomes tardy, then it is better not to execute that job rather than completing it late.
Laxity Type

## Slide 28: Resource Parameters
Premptivity of Resources
Exclusive/Shared Resources
Resource Graph
  Connectivity
  A part of edge
Computer
MEM
RAM
ROM
CPU
Comp
CPU
Display
Mem

## Slide 29
Preemptivity of Resources
A resource is nonpreemptible if each unit of the resource is constrained to be used serially. It means if a nonpreemptible resource is allocated to a job, other jobs needing it must wait until the current jobs complete its use.
If jobs can use every unit of the resource in an interleaved manner, then the resource is preemptible.
Resource Parameter

## Slide 30
A valid schedule is feasible schedule if every job completes by its deadline.
A set of job is schedulable according to a scheduling algorithm if when using the algorithm the scheduler always produces a feasible schedule.
A hard real-time scheduling algorithm is said to be optimal if using this algorithm the scheduler always produces a feasible schedule if the given set of jobs has feasible schedule.
Other than the above other performance measures used are: Maximum and average
  Tardiness,
  Lateness,
  Response time,
  Miss, Loss and Invalid rates.
Feasibility, Optimality and Performance Measures

## Slide 31
Lateness of a job is the difference between its completion time and the deadline (i.e. completion time – deadline). It can become negative if the job completes early and positive it completes late.
For a set of jobs in the system, the response time of the job which completes last, is called makespan of the schedule.
Makespan is used to compare scheduling algorithm performance. The algorithm which produces a schedule with a shorter makespan is better.
Most frequently used performance measure for jobs that have soft deadlines is their average response time.
For some soft real-time systems, it is acceptable to complete some jobs late or to discard late jobs. For those systems, a suitable performance measure include the miss rate (% of jobs those complete late) or loss rate (% of jobs those are discarded)
Invalid rate = Loss rate + Miss rate : It should be minimized
Feasibility, Optimality and Performance Measures (contd.)

## Slide 32: Schedule

## Slide 33: What is scheduling ??
Tasks have timing constraints
Execution is bounded by max delay
Ensure that time bound is respected as imperatively as possible
Objective – allow tasks to fulfill timing constraints when running in nominal mode

## Slide 34: Valid schedule
A valid schedule satisfies the following requirements
  every processor is assigned to at most one job at any time
  every job is assigned to at most one processor at any time
  No job is scheduled before its release time
  Depending on the scheduling algo(s) used- total amount of processor time assigned to every job is equal to its max or actual execution time
  All the precedence & resource usage constraints are satisfied

## Slide 35: Some Terminology
Valid Schedule
Feasible Schedule
Proficient Scheduler
Optimal Scheduler
Scheduling Pts.
Pre-emptive Scheduling
Utilization
Jitter

## Slide 36: Scheduling Algo. Taxonomy
Online/Offline Scheduling (Static/Dynamic)
    Deterministic
    Less complexity
    Flexibility
  Online-used
    Dynamic variations in user demand/resources
    Future loads unpredictable
    More overhead
    Less precise
    Optimal schedule not possible
  Online – overloaded – clairvoyant scheduler!

## Slide 37: Scheduling algo. Taxonomy
Preemptive / Non-preemptive
  Preemptive disadvantages
    Overhead Involved
  Non-preemptive advantages
    Sharing of resources easier
  Non-preemptive disadvantages
    No optimal schedule possible
Best Effort/ Timing Fault Intolerant
Centralized/Distributive

## Slide 38: Feasibility
Valid schedule is feasible if all tasks are completed on time

## Slide 39: Performance Measure
Schedulable task set
Optimal
Lateness
Avg absolute lateness
Make span
Avg response Time
Miss Rate
Loss Rate
Invalid Rate

## Slide 40
Scheduler does not run continuously but at scheduling pts

## Slide 41: Scheduler Implementations
Election Table
Priority Queuing list
Constant/ Varying Priority
  Constant
    Completion time
    Relative deadline
    Period
  Variable
    Pending computation time
    Residual laxity
    Absolute deadline /release time (effective)

## Slide 42
Effective Release Time
  ERT = ART if no predecessor
  ERT = max(ART, RT of all its predecessor)
Effective Deadline Time
  EDT = ADT if no successor
  EDT = min(ADT, DT of all its successors)

## Slide 43
J1 (2,10)
J2 (0,7)
J3 (1,12)
J4 (4,9)
J5 (1,8)
J6 (0,20)
J7 (6,21)
Does this satisfy basic requirements ??

## Slide 44
Any Questions?
Thank You.