## Slide 1: RMA & EDF Examples

## Slide 2
Priority-driven Preemptive Scheduling
Assumptions & Definitions
Tasks are periodic
No aperiodic or sporadic tasks
Job (instance) deadline = end of period
No resource constraints
Tasks are preemptable
Laxity of a Task
Ti = di – (t + ci’)
where di: deadline;
t : current time;
ci’ : remaining computation time.
t
C’i
Laxity
di

## Slide 3
Rate Monotonic Scheduling (RMS)
Schedulability check (off-line)
- A set of n tasks is schedulable on a uniprocessor by the RMS algorithm if the processor utilization (utilization test):
The term n(21/n -1) approaches ln 2, (0.69 as n  ).
- This condition is sufficient, but not necessary.

## Slide 4
RMS (cont.)
Schedule construction (online)
- Task with the smallest period is assigned the highest priority.
- At any time, the highest priority task is executed.
RMS is an optimal preemptive scheduling algorithm with fixed priorities.
Static/fixed priority algorithm assigns the same priority to all the jobs (instances) in each task.

## Slide 5
RMS Scheduler -- Example 1
Task set: Ti = (ci, pi)
T1 = (2,4) and T2 = (1,8)
Schedulability check:
2/4 + 1/8 = 0.5 + 0.125 = 0.625 ≤ 2(√2 -1) = 0. 82
T11
T21
T12
0
2
3
4
6
8
Active Tasks :
{T1, T2}
Active Tasks :
{T2}
Active Tasks :
{T1}

## Slide 6
RMS Scheduler -- Example 1
Task set: Ti = (ci, pi)
T1 = (2,4) and T2 = (1,8)
Schedulability check:
2/4 + 1/8 = 0.5 + 0.125 = 0.625 ≤ 2(√2 -1) = 0. 82
T11
T21
T12
0
2
3
4
6
8
Active Tasks :
{T1, T2}
Active Tasks :
{T2}
Active Tasks :
{T1}

## Slide 7
RMS scheduler -- Example-2
Task set: Ti = (ci, pi)
T1 = (2,4) and T2 = (4,8)
Schedulability check:
2/4 + 4/8 = 0.5 + 0.5 = 1.0 > 2(√2 -1) = 0. 82
T11
T21
T12
0
2
3
4
6
8
Active Tasks :
{T1, T2}
Active Tasks :
{T2}
Active Tasks :
{T2, T1}
T21
Active Tasks :
{T2}
Some task sets that FAIL the utilization-based schedulability test are also schedulable under RMS  We need exact analysis (necessary & sufficient)

## Slide 8
Earliest Deadline First (EDF)
Schedulability check (off-line)
- A set of n tasks is schedulable on a uniprocessor by the EDF algorithm if the processor utilization.
This condition is both necessary and sufficient.
Least Laxity First (LLF) algorithm has the same schedulability check.

## Slide 9
EDF/LLF (cont.)
Schedule construction (online)
  EDF/LLF: Task with the smallest deadline/laxity is assigned the highest priority.
  At any time, the highest priority task is executed.
EDF/LLF is an optimal preemptive scheduling algorithm with dynamic priorities.
Dynamic priority algorithm assigns different priorities to the individual jobs (instances) in each task.

## Slide 10
EDF scheduler -- Example
Task set: Ti = (ci, pi, di)
T1 = (1,3,3) and T2 = (4,6,6)
Schedulability check:
1/3 + 4/6 = 0.33 + 0.67 = 1.0
T11
T21
T12
0
1
5
6
Active Tasks :
{T1, T2}
Active Tasks :
{T2}
Active Tasks :
{T2, T1}
Active Tasks :
{T1}
Unlike RMS, Only those task sets which pass the schedulability test are schedulable under EDF
3
T21

## Slide 11
RMS vs. EDF/LLF
RMS is an optimal preemptive scheduling algorithm with fixed priorities.
EDF/LLF is an optimal preemptive scheduling algorithm with dynamic priorities.
RMS schedulability properties can be analyzed; rich theory exists and it is widely used in practice.
EDF/LLF offers higher schedulability than RMS, but it is more difficult to implement.

## Slide 12
RMS & EDF -- Example
0
5
10
15
20
25
30
35
0
7
14
21
28
35
T1
T2
RMS schedule
0
5
10
15
20
25
30
35
0
7
14
21
28
35
T1
T2
EDF schedule
Deadline miss
Process
Period,
T
WCET,
C
T
1
5
2
T
2
7
4

## Slide 14: Schedulability: UB Test
Utilization bound (UB) test: a set of n independent periodic tasks scheduled by the rate monotonic algorithm will always meet its deadlines, for all task phasings, if
U(1) = 1.0 U(4) = 0.756 U(7) = 0.728
U(2) = 0.828 U(5) = 0.743 U(8) = 0.724
U(3) = 0.779 U(6) = 0.734 U(9) = 0.720
For harmonic task sets, the utilization bound is U(n)=1.00 for all n.
--- + .... + --- < U(n) = n(2 - 1)
C1 Cn 1/ n
T1 Tn
Notes: 6
We say a set of tasks is schedulable if the task set is guaranteed to meet all its deadlines. The utilization bound test says that a task set is schedulable if its total utilization is less than a certain bound, called the Liu & Leyland bound. The utilization bound test provides the basic formula underlying the theory. More complex formulas provide better bounds. This test is the application of a theorem, which was proved by Liu and Leyland in “Scheduling Algorithms for Multiprogramming in a Hard Real-Time Environment”, JACM, 1973.
The utilization bound test assumes that:
1. The processor always executes the highest priority task.
2. Task priorities are assigned according to rate monotonic policy.
3. Tasks do not synchronize with each other.
4. Each task’s deadline is at the end of its period.
5. Tasks do not suspend themselves in the middle of computations.
The test takes into account the preemption time and execution time for each task under a worst-case combination of periods and execution times. As the number of tasks goes to infinity, the bound approaches ln(2) = 0.693; in other words, any number of independent periodic tasks will meet their deadlines if the total system utilization is under 69%
For a harmonic task set (in which the period of each task is a multiple of all higher-frequency tasks), the utilization bound is 1.0 for all task sets.

## Slide 15: Sample Problem: Applying UB Test
Total utilization is .200 + .267 + .286 = .753 < U(3) = .779
The periodic tasks in the sample problem are schedulable according to the UB test
 | C | T | U
Task t1 | 20 | 100 | 0.200
Task t2 | 40 | 150 | 0.267
Task t3 | 100 | 350 | 0.286
Notes: 7
Since we are interested in worst-case behavior, tasks utilizations are always rounded up. For example, U2 = 40/150 = .2666... becomes .267 and U3 = 100/350 = .2857143... becomes .286.
In this example, since the total utilization is under the bound for three tasks, all tasks are guaranteed to meet their deadlines, even under worst-case conditions. An additional 24.7% CPU capacity is available for lower-priority tasks that have no deadline.
Remember that there are several assumptions associated with the utilization bound test:
Zero context switch overhead.
Deadlines are at end of period.
No interrupts are used.
Priorities are assigned in rate monotonic order.
Tasks do not interact with one another.
Tasks do not suspend themselves.

## Slide 16: Timeline for Sample Problem
0
100
200
300
400
Scheduling Points
t
2
t
3
t
1
Notes: 8
This is the timeline for the periodic tasks of the sample problem (shown on the previous page), in which tasks are lined up in worst-case phasing (i.e. all task are ready to execute at time t=0).
Timelines show one possible execution schedule and provide a graphical view of schedule analysis. We will draw timelines according to the following conventions:
Tasks are arranged and numbered in rate monotonic order, highest frequency at the top.
We assume Liu and Leyland “worst-case” phasing, where all tasks start at time t=0.
Execution time for t1 is plotted on its line.
Execution time for t2 is then plotted on its line, accommodating preemption from t1’s execution; then this process is repeated for remaining tasks.
If any task is preempted, its execution time block is divided with a hole in the middle representing the preemption (e.g. t3)

## Slide 17: Exercise: Applying the UB Test
a. What is the total utilization?
b. Is the task set schedulable?
c. Draw the timeline.
d. What is the total utilization if C3 = 2 ?
Given:
Notes: 7
Since we are interested in worst-case behavior, tasks utilizations are always rounded up. For example, U2 = 40/150 = .2666... becomes .267 and U3 = 100/350 = .2857143... becomes .286.
In this example, since the total utilization is under the bound for three tasks, all tasks are guaranteed to meet their deadlines, even under worst-case conditions. An additional 24.7% CPU capacity is available for lower-priority tasks that have no deadline.
Remember that there are several assumptions associated with the utilization bound test:
Zero context switch overhead.
Deadlines are at end of period.
No interrupts are used.
Priorities are assigned in rate monotonic order.
Tasks do not interact with one another.
Tasks do not suspend themselves.

## Slide 18: Solution: Applying the UB Test
a. What is the total utilization? .25 + .34 + .10 = .69
b. Is the task set schedulable? Yes: .69 < U(3) = .779
c. Draw the timeline.
d. What is the total utilization if C3 = 2 ?
.25 + .34 + .20 = .79 > U(3) = .779
0
5
10
15
20
Task t1
Task t3
Task t2
Notes: 8
This is the timeline for the periodic tasks of the sample problem (shown on the previous page), in which tasks are lined up in worst-case phasing (i.e. all task are ready to execute at time t=0).
Timelines show one possible execution schedule and provide a graphical view of schedule analysis. We will draw timelines according to the following conventions:
Tasks are arranged and numbered in rate monotonic order, highest frequency at the top.
We assume Liu and Leyland “worst-case” phasing, where all tasks start at time t=0.
Execution time for t1 is plotted on its line.
Execution time for t2 is then plotted on its line, accommodating preemption from t1’s execution; then this process is repeated for remaining tasks.
If any task is preempted, its execution time block is divided with a hole in the middle representing the preemption (e.g. t3)

## Slide 19: Toward a More Precise Test
UB test has three possible outcomes:
0 < U < U(n)  Success
U(n) < U < 1.00  Inconclusive
1.00 < U  Overload
UB test is conservative.
A more precise test can be applied.
Notes: 9
The results of applying the UB test can be:
0<U<u(n) success, task set is schedulable
U9n)<U<1.0 inconclusive, task set may or may not be schedulable
1.0 < U overload, task set exceeds capacity
When the UB test is inconclusive, a more precise test can be applied.
The previous schedulability test (utilization bound test) is very conservative. Schedulable system utilization can often exceed 90%. In fact, for tasks with harmonic periods, where each period is evenly divisible into all longer periods (e.g. 100 ms, 200 ms, 800 ms, 1600 ms), the utilization bound is 100%.